NWAVETEC DEVELOPMENT KIT V3
USER MANUAL

# 1. Main features of this Development Kit
3.

  USB
  Jumpers J1, J2, J3
  X4 Pinouts Connector
  X2 Antenna Connector
  X3 JTAG Connector
18. Easy USB connection to PC or direct UART interface
19. AT-commands set via UART / USB-Serial to work in the modem mode
20. Capability to embed up to 32KB* of user firmware on MCU flash including communication API supplied as a library
21. Access to all Cortex-M3 features and the EFM32G210F128 or EFM32TG210F32 MCU peripherals
22. Programming templates and examples of simple telemetry applications
23. Support for ARM Cortex Microcontroller Software Interface Standard (CMSIS)
24. * The firmware code size can be up to 128KB according to this MCU flash size and NWAVE library size is about 9Kb only. There is a limitation of code size caused by IAR compiler free license which is 32Kb as maximum of compilable code. The full license has no such a limitation and can be purchased from IAR. However, there is no code size limitation when project is built in Simplicity Studio using GNU C Compiler (gcc). The gcc is not limited by code size. In the current version of the Development Kit user package both IAR EW and Simplicity Studio with gcc are supported.
# 2. Getting Started
26. Here is a Quick Start instruction describing how to send NWAVE messages.
## 2. 1. IAR Embedded Workbench (IAR EW) Installation
27. For getting an evaluation software follow the next link:
29. http://supp.iar.com/Download/SW/?item=EWARM-EVAL
31. After starting IAR EW you will be offered to select a license type: a 30-day time limitation or a 32Kbytes code size limitation.
## 2. 2. Simplicity Studio installation
34. Download Simplicity Studio from the next link:
35. http://www.silabs.com/products/mcu/Pages/simplicity-studio.aspx
36. After installation and first start let the software complete the updates downloading.

## 2. 3. Getting Git
3. http://git-scm.com/download/win
5. Run the installation.
7. Tick Git Bash Here and Git GUI Here.
24. Select the command line option.
39. Note: if you select the last option it is going to override Windows tools like “find” and “sort”
41. Select the line ending conversions.
## 2. 4. Getting NWAVE example for IAE EW from Git repository
58. Git has two interfaces: Command Line and GUI.
60. Getting a repository from the Command Line Interface run Git Bash
62. Type: git clone https://github.com/NWAVETEC/nwave.git
78. If you
80. Check the content of this directory (run ls) it should show files:
97. Getting a repository form the GUI run Git GUI.
99. At the first start select Clone Existing Repository
121. Type in the repository name and the directory name which will be created after this step.
134. Press Clone and it will show the process of getting a repository.
147. Then it finishes with showing this window below, now the project files are placed in the given directory:
## 2. 5. Open Workspace in IAR EW
160. Open a workspace with file nwave_rm3_templates.eww which is placed at the top level of the cloned nwave directory.
## 2. 6. Open Workspace in Simplicity Studio
162. Run Simplicity IDE and click menu File->Switch to Workspace->other and select subfolder called Simplicity Studio under clonned nwave folder.
## 2. 7. Open main.c file and select an example
163. Select an example by editing this string:
164. #define EXAMPLE_CODE UART_2_RM
166. the UART_2_RM means to include a simple example code which demonstrates how to use NWAVE API, in particular sending upcoming to UART data directly to the radio module transmitter.
168. the AT_PARSER means to include an example code of the parser of AT-commands which allows user to operate with the transmitter by AT-commands. The parser listens to the specific AT-commands on the serial port. These commands are described below in AT-Commands section.
## 2. 8. Connection J-Link programmer to the Development Kit
188.

  JTAG J-Link Cable
  to X3 connector
  USB to PC
## 2. 9. Compile and Flash the device in IAR EW
196. In open project press F7 to compile it or CTRL+D to compile, flash and debug the device *. The same action can be performed via Download and Debug button, see at the picture:
198. * To Download and Debug in hardware you need to connect JTAG J-Link adapter (or any starter kit, for instance, STK3200 or STK3300) to the X3 connector. Otherwise it is possible to trace the firmware code in Simulator which can be alternatively chosen in Debug option of the project. By default it is set to JTAG J-Link adapter.
## 2. 10. Compile project in Simplicity Studio
201. Having a project open click at the build button to compile as it is shown at the picture below/
## 2. 11. Create a connection in serial terminal programme
207. Connect the Development Kit to the USB port of your computer. The Development Kit has a USB-to-Serial converter so it should appear as an additional serial port in the device list on your system.
208. In your terminal programme* create a new connection, select this new serial port and and set the parameters for the connection as below:
209. Baud rate: 9600
210. Data bits: 8
211. Stop bits: 1
212. Parity: none
213. Handshake(Flow Control) Hardware: none
214. Handshake(Flow Control) Software: none
216. * Tera Term or Putty can be used as terminal programmes free of charge.
## 2. 12. Sending NWAVE messages
217. The API of NWAVE Library is described in the section NWAVE Library API.
219. Depending on selected example code in main.c file by defines AT_PARSER or UART_2_RM user can input either AT-Commands or data bytes directly to the radio transmitter. Both examples demonstrate using an API of nwave_unb library and send NWAVE messages.
221. Note: In AT_PARSER example user basically needs to set carrying frequency and bandwidth in Hz by «AT+FREQ=...» command and send data by «AT+SEND=...» command. In UART_2_RM example user needs to care about setting a proper value carrying frequency by calling NWAVE_Set_Frequency(...) function (see section NWAVE Library API).
## 2. 13. User Application
223. The provided source code is a template which allows simply embed a user application. Its structure is organized as two functions user_setup() and user_loop() called from main.
224. The user_setup() is supposed to include all initialization and it is called once.
225. The user_loop() is supposed to contain user application load.
226. An example code given below shows how simple transmission of user data can be done. In this example each 4 bytes coming to UART are sent to the radio module transmitter.
227. void uart_2_rm (void)
228. {
229. int watch_c;
230. while ((watch_c = NWRM_UART_GetChar()) >= 0) {
231. send_buf_len.send_buffer[i++] = watch_c;
232. if (i >= 4) {
233. unsigned char packetRec[256];
234. #warning "Set a proper frequency value for your environment"
235. /* NWAVE_Set_Frequency(866500000, 50000, 100); */
236. NWAVE_Set_Frequency(868800000, 50000, 100);
237. NWAVE_send(send_buf_len.send_buffer, 4 /*send_buf_len.len*/ , packetRec, PROTOCOL_B);
238. tfp_printf("Data sent.\n");
239. i = 0;
240. }
241. }
242. }
243. void user_loop (void)
244. {
245. uart_2_rm();
246. }
247. int main(void)
248. {
249. user_setup();
250. while (1) {
251. NWRM_RTC_Sleep();
252. user_loop();
253. }
254. }
# 3. AT-Commands
## 3. 1. Setting carrying frequency and bandwidth
258. Syntax:
260. «AT+FREQ=[Carrying_frequency],[Bandwidth]»
262. Carrying_frequency - central carrying frequency in Hz
264. Bandwidth - half-range which is added to and subtracted from central carrier frequency giving a full range in a result.
266. Example: AT+FREQ=868000000,25000
268. If success it returns «Ok», if failed - «Error»
## 3. 2. Sending messages by NWAVE protocol
271. Syntax:
273. «AT+SEND=[&hex_byte1][&hex_byte2]..[ [&hex_byteN]]»
275. hex_byte - hexadecimal representation of the byte. Before each hexadecimal byte the symbol «$» is placed.
277. Example: AT+SEND=$23$0A$5D$5F
279. If success it returns «Ok», if failed - «Error»
## 3. 3. Getting a serial number
281. Syntax:
283. «AT+SERIAL=?»
285. Example: AT+SERIAL=?
287. If success it returns a serial number of the device, e.g. «0000F556», if failed - «Error»
# 4. NWAVE Library API
290. The NWAVE Library is provided as a compiled library and it is stored in the nwave_unb.lib file. It is linked to the project. The unb.h is a header file with definitions for C functions of the library. It contains next function definitions:
## 4. 1. Setting carrying frequency and bandwidth
292. int NWAVE_Frequency_Set(unsigned long carrying_frequency, unsigned long bandwidth, int channels);
294. carrying_frequency – frequency of the low end of a range
295. bandwidth – frequency of the high end of a range
296. channels – channels number
## 4. 2. Sending messages by NWAVE protocol
299. unsigned char NWAVE_send(unsigned char *packet, unsigned char length, unsigned char* packetRec, unsigned char protocol);
300. packet – pointer to the buffer for transmission
301. length – lengеh of the transmitted buffer
302. packetRec – pointer to the reading back buffer for future implementation of Protocol E
303. protocol – protocol type, is chosen by defined constants: PROTOCOL_B or PROTOCOL_E
306. NOTE: User should not interrupt the execution of this function for more than 200us.
# 5. Peripheral Devices Sharing
309. On this Development Kit the USART 0 is used for communication with the radio device.
310. The CP2102 is the USB to Serial converter which is connected to the Low Energy UART of the MCU. It also converts 5V level of USB to the 3.3V level for the board power supply. This power supply line can be disconnected by removing J3 jumper. The RX and TX lines can be disconnected by removing J1, J2 jumpers.
311. The Table 1 shows the pinout assignments on X4.
## Table 1. The Device Pinout on X4
X4 Pin # and Name		Pin Functionality Alternatives	MCU Pin # and Name
Pin #	Pin Name		Pin #	Pin Name
1	GND
2	VDD
3	PC0	ACMP0_CH0, PCNT0_S0IN, US1_TX	5	PC0
4	PA1	TIM0_CC1, I2C0_SCL, CMU_OUT1	2	PA1
5	PA0	TIM0_CC0, I2C0_SDA	1	PA0
6	PF1	DBG_SWDIO, LETIM0_OUT1	26	PF1
7	PF0	DBG_SWCLK, LETIM0_OUT0	25	PF0
8	PC14	ACMP1_CH6, TIM0_CDTI1, TIM1_CC1, PCNT0_S1IN	23	PC14
9	PC1	ACMP0_CH1, PCNT0_S1IN, US1_RX0	6	PC1
10	PB11	DAC0_OUT0, LETIM0_OUT0	10	PB11
11	PB13	HFXTAL_P, LEU0_TX	12	PB13
12	PC15	ACMP1_CH7, DBG_SWV, TIM0_CDTI2, TIM1_CC2	24	PC15
13	PD4	ADC0_CH4, LEU0_TX	16	PD4
14	PD5	ADC0_CH5, LEU0_RX	17	PD5
15	PD6	ADC0_CH6, LETIM0_OUT0, I2C0_SDA	18	PD6
16	PD7	ADC0_CH7, LETIM0_OUT1, I2C0_SCL	19	PD7

2. The Table 2 shows the pinout assignments on X3.
## Table 2. The Device Pinout on X3
X3 Pin # and Name		Pin Functionality Alternatives
Pin #	Pin Name
1	VDD
2	GND
3
4	GND
5
6	GND
7	DB2	DBG_SWDIO, LETIM0_OUT1
8	GND
9	DB3	DBG_SWCLK, LETIM0_OUT0
10	GND
11
12	GND
13
14	GND
15	RST
16	GND
17
18
19
20	GND

# 6. Electrical Scheme
2. The figure below is an electric circuit diagram of the NWAVE development kit.
# 7. Bill of Materials
12. The table below is a list of used mechanical and electronic components and their parameters.